How to setup Wireless WAN Function of F300

Product line: wireless    question category: function config

Part 1: Login the homepage of the router

Part 2: Setup connection type and LAN IP

Part 3: Enable Wireless WAN function

Part 4: Setup secondary SSID and security key

The Topology is as below:

Steps are as following:

1.1 Login to the management page of the router.

1.2 The login password is admin, then click Advanced.

2.1 Click Advanced, then click Internet connection setup. Choose DHCP, click Save.

2.2 Click Advanced, and then click LAN Settings. Change your router’s LAN IP.(The LAN IP address should be in different network segment. For example, the router1 has the LAN IP 192.168.0.1, then you can set the router2’s LAN IP as 192.168.1.1.)

3.1 Click Advanced and then choose WAN Medium Type, choose Wireless WAN, Click Open Scan.

3.2 Select the Router1’s SSID, and input the router1’s security key. then click OK to save the settings.

3.3 After reboot, if the connection status shows connected and get the gateway of uplink router, it means that you can have internet.

Note: After finish the Wireless WAN settings, the primary SSID will become secondary SSID automatically.

4.1 Click Wireless and Wireless Basic Setting, change secondary SSID as you want, and then click OK to save all the settings.

4.2 Click wireless security key, select SSID which you have set as secondary SSID, choose the security mode as WPA-PSK, input your security key, and click OK to save all the setting.

Notice：If you have other PC need to be get connected, please connect it to the one of the LAN port or the wireless signal of the router. There is no need to configure the router again.