The document applies to users of the "O3 Mode Settings"

Product Line：Tenda Outdoor Wireless Bridge O3         Question Category ：Function Configure

Part 1：Configure your computer

Part 2: Login management interface of O3

Part 3：Select the proper operating mode

- Mode one：AP Mode ：Transform your existing wired network to a wireless network.

- Mode two：Station Mode：Acting as a “Wireless Adapter” to connect your wired devices to a wireless network.

- Mode three：Universal Repeater Mode：Extend your existing wireless coverage by relaying wireless signal.

- Mode four：WISP：Wirelessly connect to ISP station/hotspot to share Internet to local wireless and wired network.

- Mode five：Repeater：Combine multi networks via wireless connection.

- Mode six：P2MP Mode：Combine multi local networks via wireless connection.

- Mode seven：Router Mode：Wired connect to ADSL/Cable Modem via WAN port and share Internet to local wireless and wired network.

1.1 Right click icon in the lower right corner of the desktop computer, and select “Open Network and Sharing Center”.

1.2 Select and click corresponding network adapter.

1.3 Click “Status” and then click “Properties”.

1.4 Double click “Internet protocol IPV4” And select “Use the following IP address”, “192.168.2.X” （X is an integer between 3~253），Subnet mask is “255.255.255.0”.

2.1 Login AP mode

Input 192.168.2.1 in a web browser’s address bar, and then press Enter or Return on your keyboard. Enter the default username and password (admin for both defaults) and click Login.

3.1 Mode One ：AP Mode

Click “Quick setup”, select “AP Mode”.

Custom local wireless network parameters and click next.

Confirm the information is correct, click "Save"

3.2 Mode two ：Station mode

Select “Station mode” in “Quick Setup” option.

Open scan button, select the superior wireless signal which you want to extend.

The information in the frame as below should be the same with superior router.

Configure local IP address, confirm it is different from superior router but in a same segment network. DNS can be reference.

Confirm the information is correct, click "Save"

3.3 Mode Three：Universal Repeater mode

Select “Universal Repeater mode” in” Quick Setup” option.

Open scan button, select the superior wireless signal which you want to extend.

The information in the frame as below should be the same with superior router.

Configure local IP address, confirm it is different from superior router but in a same segment network. DNS can be reference.

Confirm the information is correct, click "Save"

3.4 Mode four ：WISP mode

Select “WISP mode” in “Quick Setup” option.

Open scan button, select the superior wireless signal which you want to extend.

The information in the frame as below should be the same with superior router.

Select the appropriate network connection type and fill in corresponding information

Custom local wireless network parameters, as below:

Configure local IP address, confirm it is not in the same network segment with the superior router and click next.

Confirm the information is correct, click "Save"

3.5 Mode five ：Repeater mode

Select “Repeater mode” in “Quick Setup” option.

Open scan button, select the superior wireless signal which you want to extend.

The information in the frame as below should be the same with superior router.

Configure local IP address, confirm it is different from superior router but in a same segment network. DNS can be reference.

Confirm the information is correct, click "Save"

3.6 Mode Six ：P2MP mode

Select “P2MP mode” in “Quick Setup” option.

Open scan button, select the superior wireless signal which you want to extend.

The information in the frame as below should be the same with superior router.

Configure local IP address, confirm it is different from superior router but in a same segment network. DNS can be reference.

Confirm the information is correct, click "Save"

3.7 Mode Seven ：Router mode

Select “Router mode” in “Quick Setup” option.

Select appropriate Wan Connection Type, for example PPPOE and fill in username and password. And click next.

Custom local wireless network parameters and click next.

Confirm the information is correct, and click “Save”.