How to Setup DSL Dial Up on D151

Model: D151           Question Classification: Internet Setting

Step 1: Physical Connection

Step 2: Configure the Computer

Step 3: Configure the Modem router

Step 4: Check whether it’s connecting

Connect telephone line to the DSL port the modem, and then connect computer to 2/3/4 any of the LAN ports. Physical connection shows as below.

Note: When modem router is normally working, the SYS light is blinking, WAN light is solid on or blinking, and the relevant LAN light is also blinking.

1. Right Click on Network Connection Icon on the system bar, then click on Open Network and Sharing Center.

2. Click on Change Adapter Settings.

3. Right click on Local Area Connection, then choose the Properties option.

4. Double click on Internet Protocol Version 4(TCP/IPv4).

5. Choose Obtain an IP address automatically and Obtain DNS server address automatically and then click OK.

6 Also click on OK on the previous Local Connection Properties window.

- Open a web browser, and type 192.168.1.1 in the address bar, press Enter. The login User name and Password both are “admin”.

- After login to the interface, (1) choose DSL on Link Type, and PPPoE on Connection Type. (2) choose the relevant Country and ISP, confirm the VPI/VCP value. (3) type in the username and password. (4) finish wireless setup. (5) Save the configuration.

- The connection status will show as “connected” if it dial up successfully.

Click “Advanced”- “WAN”-“IPV4 Address”, if you have received a public IP address, that means you can access to the internet.