How to setup the Portal Authentication

Model number: G3

This article will guide you how to setup the Portal Authentication.

Part 1: Enter to the Portal Authentication interface

Part 2: Create an account for authentication user

Part 3: Set the login push page

Part 4: Launch a browser to surf the Internet

- Click Portal Authentication to enter the configuration interface, and enable Portal Authentication.

- Enter the IP address(es) or MAC address(es) which are set to be free of authentication in the white list field.

- Click to create an account for authentication user, configure the account info, and click to apply your settings.

- Now, an account is set successfully, and the detail will be shown in the list.

- After the portal authentication is set OK, you can click Advertisement to set the login push page.

- Now, if you (your host IP address is not included in the white list of portal authentication) want to surf the Internet and you launch a browser, the web page may be shown as below which requests you entering the account username and password set in portal authentication section.

- This page allows you to view the authenticated user connecting to the router or an AP managed by the router when portal authentication is enabled.