How to Setup Universal Repeater Mode

This document applies for the users that want to setup universal repeater function

Model Number: N301/F3/FH456        Question Classification: Function Settings

Part 1：Configure IP address of your computer

Part 2：Login to the setup page

Part 3：Setup Universal Repeater function

Part 4: Check whether you can surf the internet

1. Click on Network Connection Icon on the system bar, then click on Open Network and Sharing Center.

2. Click on Change Adapter Settings.

3. Right click on Local Area Connection, then choose the Properties option.

4. Double click on Internet Protocol Version 4(TCP/IPv4).

5. Choose Obtain an IP address automatically and Obtain DNS server address automatically and then click OK.

6 Also click on OK on the first Local Connection Properties window.

Notice：If you use the router for the first time, it will appear easy to use interface in the process of you set Universal Repeater mode, you need to skip these interface, go to the advanced Settings interface to set.

1.Open a browser then type 192.168.0.1 in the Address Bar, press Enter，and login to the router interface.

- Click the "Skip" or “Next”.

- Set router’s SSID and wireless password, and click Next, refer to the following steps.

4. “Saving…please wait…” Wait about 10 seconds, it will come out an interface. Click “More” to go to advanced setting page.

1. Enter the router's setting interface，click “Wireless Repeating”. choose bridge mode as “Universal Repeater”, select your uplink wifi signal, type wifi password of your uplink router, click “OK” to save all the settings. Then click “OK” on the pop-up window.

2. After click OK, the router will reboot automatically.

Notice：For the convenience of management, when you setup Universal Repeater mode, we have to make sure this router’s IP address is different from uplink router’s address, but in the same network segment. Such as if the uplink router’s IP address is 192.168.2.1, we have to change this router’s IP address to 192.168.2.X, X∈(2~254).

After reboot, connect router’s LAN1/LAN2/LAN3 ports, or reconnect wireless signal of the router, try whether you can surf the internet.