O3 v2.0-- How to use in outdoor monitoring (one to Multi)

Note: This article will guide you how to use O3 in outdoor monitoring and the steps as below.

Step 1: Connect the device as the topology

The topology is shown below:

1.1 The O3 sender is connected to the camera with the Ethernet cable, the working mode is AP mode.

1.2 The O3 receivers are connected to the switch, NVR and other equipment with the Ethernet cable, the working mode is Client mode.

Note:

a: A sender can correspond to three receivers mostly.

b: The O3 antenna is a directional antenna. The O3 position of the sender and the receiver must be opposite.

Step 2: Setup the corresponding operating mode

2.1 Setup AP mode on the O3 sender. If you do not know how to setup AP mode on the O3, refer to O3V2.0- How to setup AP mode

2.2 Setup Client mode on the O3 receivers and connect the wireless signal of the O3 sender. If you do not know how to setup Client mode on the O3, refer to O3V2.0-How to setup Client mode

Step 3: Confirm that the O3 configuration is successful

3.1 Check whether the configuration is successful, please check the indicators, if the indicators of O3 sender are always on and the indicators of O3 are blinking, the configuration success.

3.2 After the configuration. Please check whether the configuration is successfully, login in the Setting page of the O3 receivers, click “Status”.