How to Change Wireless SSID and Security Key

This document applies to users who need to change wireless SSID and security key.

Model: Tenda N301/F3/FH456         Problem classification: wireless setting

Step 1: Open a browser on your computer, input 192.168.0.1 in address bar, then press enter button on your keyboard, enter login password, click “Login”.

Step 2: Click “Wireless”, to manage your wireless network. The reference as below:

### WiFi ON/OFF Button

The WiFi ON/OFF button allows you to turn on/off your WiFi. It is enabled by default.

Log in to the Router’s User Interface, click Wireless. Click WiFi ON/OFF button to enable/disable your WiFi, and click OK on the bottom of the page to activate the settings.

### Change your WiFi name/password

This part allows you to change your WiFi name, select your wireless security mode, and set up or change your WiFi password. Remember to click OK on the bottom of the page to save the settings you configure.

Hide WiFi: If the Hide WiFi option is checked, the wireless devices cannot search the WiFi name of the Router. To connect to your Router’s WiFi, you need know the WiFi name in advance and enter the WiFi name on each wireless client manually.

Security Mode: The router offers three security modes: WPA-PSK, WPA2-PSK (Recommended), and WPA/WPA2-PSK Mixed. You can select one according to your needs. Or you can select None to share your WiFi with others without requiring a password. There is no WiFi password and security mode set by default. But if you set up a WiFi password in Quick Setup Wizard, the security mode will be changed to WPA2-PSK (Recommended).

### WiFi Signal Strength

The Router offers two levels of signal strength: low and high (default). Select Low if it can satisfy you. Standard offers the widest coverage range while High has strong capability of penetrating wall. Select one from them according to your needs. Remember to click OK on the bottom of the page to save the settings you configure.